## Slide 1
From Oracle to Parquet and Spark:
Enabling Scalable Access and Analysis of ATLAS DCS Data
ATLAS Scope meeting
February 12th, 2026
Luca Canali, ADAM and ATLAS-DBA

## Slide 2: Luca Canali – A Brief Intro
DBA and Data Engineer
I am part of the ATLAS DBA team
  I work on ATLAS Oracle DBs, helping ATLAS developers and database users, under ADAM coordination
  I work on helping ATLAS users with using Spark, Hadoop, SWAN

## Slide 3: Analysis of DCS Data
DCS data mostly used for online operations
  Optimized for writes
  We only read small chunks of data, for monitoring, etc
Can we get insights by analyzing large chunks of DCS data?
  Working with detector experts for the analyses
Toolset
  Let’s not use the DB (Oracle) for this (for stability of online operations, cost, performance)
  Solution: import data into a separate and optimized platform for data analysis
DCS data in Oracle

## Slide 4: Offloading Data from Oracle for Analytics
Key idea: moving data from databases to platforms for analytics
  Export from DBs into files (Parquet format)
  Query data with scalable engines (Apache Spark)
  Worked with RUCIO, EventIndex, ATLAS DCS and NSW
From Oracle tables to Parquet files
Python jobs and/or notebooks
Oracle DB
Compute and storage on Hadoop and/or Cloud

## Slide 5: DCS Schemas Offloaded to Parquet
Data is copied from Oracle to Parquet files
  Files hosted in a Hadoop cluster provided by CERN IT (a general-purpose cluster called Analytix)
  Whole PVSS schemas exported one-off
    In addition, scheduled daily and incremental import for main table (eventhistory table)
    Detectors/DB schemas currently exported: PVSSMDT, PVSSMMG, PVSSMUO, PVSSRPC, PVSSSTG, PVSSTGC
  Eventhistory table is partitioned by timestamp values (year, month, day)
    This provides additional performance boost for selecting data of interest by timestamp range

## Slide 6: Technology: why Apache Parquet?
With Apache Spark plus Parquet files we are building a DB for large scale analysis
  High adoption in industry and open source for building data lakes and data warehouses
Parquet
  Is a columnar data format
  Optimized for storing and querying data for large-scale analysis
  Uses encoding and compression
  Data is stored together with its schema
  Works well with Apache Spark, Pandas, and many other tools
  Provides a simple way to map DB tables into files

## Slide 7: IT Services: SWAN, Spark, and Hadoop
Data analysis platform, interactive and at scale
  Running on many CPUs like batch, but interactive (notebooks)
Storage and compute (Hadoop, Spark) from CERN IT
  DCS data, used so far (Feb 2026) ~ 4 TB
  Fraction of a shared cluster capacity: 1500 cores, 21 PB
SWAN, a CERN service for Python notebooks
  https://swan.web.cern.ch/swan/
  Integrates LCG releases and Spark
  Easy to get started, build from examples

## Slide 8: End-to-End Data Analysis Platform
Users can code their data analysis in Python using scripts or Jupyter Notebooks (CERN SWAN)
Clusters are available for execution at scale Data APIs that work at scale: Data Frames and SQL
Data is prepared: This system is used as a dynamic database, importing needed information from external data sources into parquet files
(or S3)

## Slide 9: CERN SWAN architecture
Web portal
CERN Resources
EOS/CERNBox
(Data/User files)
CVMFS
(Software)
User 1
User 2
User n
...
SSO
...
SWAN as entry point to CERN computing resources
  https://swan.web.cern.ch/swan/

## Slide 10: SWAN integration with Hadoop / Spark
SWAN is connected to Hadoop & Spark clusters at CERN
  Jupyter extensions available to connect to clusters and spawn Spark executors
  Monitor the execution of Spark jobs
  Training material on Spark and SWAN: https://sparktraining.web.cern.ch/

## Slide 11: Example of Use by ATLAS Community
New Small Wheel
  Interested in analyzing DCS data imported into Parquet and joining it with COOL data among others
  A few NSW experts “onboarded” on the use of SWAN and data analytics tools
Work by ATLAS ADAM + Michelle Ann Solis (NSW)
  NSW DAQ Link Stability Investigation in 2024
  Actions: looking at several parameters monitored in the DCS to help explain instability
Details:
  Advancing ATLAS Detector Control System Data Analysis with a Modern Data Platform EPJ Web of Conferences 337, 01110 (2025)

## Slide 12: Wrap Up
DCS data from Oracle to a platform for analysis
  Pipelines are up and running, maintained by ATLAS DBA team using CERN IT infrastructure
Analysis on SWAN using Python notebooks
  Expressive APIs, run at scale on clusters
Example
  NSW task force on DAQ link stability investigations
We are happy to help detector experts to start their analysis of DCS data
Contact: atlas-dba@cern.ch

## Slide 13: References
Article:
  Advancing ATLAS Detector Control System Data Analysis with a Modern Data Platform EPJ Web of Conferences 337, 01110 (2025)
Gitlab project:
  https://gitlab.cern.ch/atlas-dba/dcs-offload
SWAN service:
  https://swan.web.cern.ch/swan/
Hadoop service:
  https://hadoop-user-guide.web.cern.ch/
Training material on Spark and SWAN
  https://sparktraining.web.cern.ch/
Acknowledgements:
  ATLAS DBA and ADAM, Andrea Formica, Michelle Ann Solis (NSW), IT services for SWAN and Spark/Hadoop